## Slide 1: Segment Routing with MPLS Data Plane
SR-MPLS
M Abdullah Al Naser
Datacom Professional
mnaser.net@gmail.com
Version 0.4

## Slide 2
The objective of this presentation is to discuss the need and benefits of Segment Routing with MPLS data plane (SR-MPLS) along with some shortcomings of LDP/RSVP-TE based MPLS in production network.
This presentation maybe useful for a network engineer running typical MPLS network for years to learn “Segment Routing” from very basic and also for a CxO to think about to move towards SDN era for the sake of service quality.

## Slide 3: MPLS Intro
SR-MPLS 101

## Slide 4: IP Based Forwarding
A method to forward packets
  Based on destination IP address
  Same lookup process at each hop takes time
Replaced Frame Relay, ATM in telecommunication network
  IP came as a best effort forwarding capability
  Variable length packet header
  Connectionless; reliability ensured by transport layer
  Flexible but has less QoS capability
TE not possible

## Slide 5: MPLS Intro
A label-based approach to forward traffic
  Labels are in a fixed 32-bit header
  Label Distribution Protocol (LDP)
    Responsible to deal with transport labels
  Label Operation: PUSH, SWAP, POP
Overlay tunnelling for customer services
  L3VPN, L2VPN
  BGP-free core; RR requires for large network
TE possible: RSVP-TE

## Slide 6: MPLS LDP
MP-BGP
R1
R2
R3
R4
CE1
CE2
Control Plane
Label distribution from R4 to R1
LDP
LDP
LDP
Local Label
404
Local Label
304
Out Label
404
Local Label
204
Out Label
304
Local Label
104
Out Label
204
Local Label
1004
Out Label
4004
Local Label
4004

## Slide 7: MPLS LDP
MP-BGP
R1
R2
R3
R4
CE1
CE2
Forwarding Plane
Traffic forwarding from R1 to R4
IP
4004
204
LDP
LDP
LDP
IP
4004
304
IP
4004
IP
IP
PHP
BGP Free Core
(RR may require in production)
IP
Label pushed
Label unchanged
Label swapped
Label popped

## Slide 8: MPLS TE
To steer traffic through longer path
  To utilize unused links
  To avoid congestion on busy links
RSVP-TE
  Creates circuits; state is signalled hop-by-hop
  Need to configure link constraints (BW and other attributes)
  Distribute TE info using IGP extension
  PCALC (CSPF) to calculate best path
  Carries TE labels to signal tunnel from head-end to tail-end PE
Push traffic into the tunnel
  Manual, Auto-route
  Tunnel fallback provides less traffic disruption

## Slide 9: MPLS TE
Shortest Path
R1
R2
R3
R4
CE1
CE2
Control Plane
RSVP PATH messages reserve BW and request for MPLS label
R5
PATH
PATH
PATH
PATH
Head-end
Tail-end

## Slide 10: MPLS TE
Shortest Path
R1
R2
R3
R4
CE1
CE2
Control Plane
RSVP RESV messages carry MPLS label
RESV
RESV
RESV
TE
Path
RESV
TE PATH is signaled “hop-by-hop” based on ERO !!!
R5
PATH
PATH
PATH
PATH
Head-end
Tail-end

## Slide 11: MPLS TE
Shortcomings:
Tunnel is not bidirectional
IGP tracks link constraints and floods periodically
  Maintains state
  TE tunnel need to be re-optimized frequently
RSVP-TE isn’t ECMP friendly (N2*K tunnel required)
  Doesn’t scale well with inter-domain (IGP) network
Additional overhead for
both router and it’s administrator
Why is RSVP-TE still useful?

## Slide 12: Fast Re-route (FRR)
Pre-computed backup path
  Backup next-hop installed in forwarding table
  Minimize reconvergence time
  Can be used to protect tunnels (links/nodes)
  Widely used in carrier backbone
Must have LFA – Loop Free Alternative
Doesn’t provide optimum path all the time
Very difficult to configure and manage

## Slide 13: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with Loop Free Alternative (LFA)
R5
1
1
2
n
IGP COST
Primary Next-hop
Backup Next-hop
1
R6
1
CE1
CE2
1
Case-1

## Slide 14: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with Loop Free Alternative (LFA)
R5
1
1
1
1
Primary Next-hop
1
R6
2
Can’t be a
Backup Next-hop
R1 itself is
R5’s next-hop
n
IGP COST
Micro-loop happens !!!
CE1
CE2
Case-2

## Slide 15: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with Remote Loop Free Alternative (RLFA)
R5
1
1
1
1
Primary Next-hop
1
R6
2
Can’t be a
Backup Next-hop
R1 itself is
R5’s next-hop
R6 can be R1’s backup next-hop
Requires LDP tunnelling for rLFA
n
IGP COST
CE1
CE2
Case-2

## Slide 16: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with RLFA is also not always Loop Free
R5
1
1
1
1
Primary Next-hop
1
R6
5
Can’t be a
Backup Next-hop
R1 itself is
R5’s next-hop
R6 can’t be R1’s backup next-hop
Because R1 itself is in R5’s transit path
n
IGP COST
We need next-gen TI-LFA
with micro-loop avoidance capability
and 100% coverage
CE1
CE2
Case-3

## Slide 17: IGP-LDP Sync
Primary Path
R1
R2
R3
R4
CE1
CE2
Primary Path Goes Down (!)
Customer traffic re-routed via alternative path
R5
LDP
LDP
LDP
LDP
Alternative
Path
My next-hop towards R4 is R5
LDP

## Slide 18: IGP-LDP Sync
Primary Path
R1
R2
R3
R4
CE1
CE2
Primary Path Goes Up (!!!)
Customer traffic dropped when re-routed via primary path – BROKEN LSP
LDP
LDP
LDP
LDP
Alternative
Path
IGP
LDP On the Way
My next-hop towards R4
is R3
IGP-LDP Sync requires to be configured on each LDP enabled link
R5

## Slide 19: FRR with RSVP-TE
SR-MPLS 101

## Slide 20: FRR with RSVP-TE
Link Protection
Primary Path
R1
R2
R3
R4
CE1
CE2
Primary
Tunnel
R6
Backup Tunnel
R5
PLR
MP

## Slide 21: FRR with RSVP-TE
Node Protection
Primary Path
R1
R2
R4
CE1
CE2
Primary
Tunnel a
R5
R6
Backup Tunnel
R3
PLR
MP

## Slide 22: FRR with RSVP-TE
SRLG Protection
Primary Path
R1
R2
R4
CE1
CE2
Primary
Tunnel a
R5
R6
Backup Tunnel
R3
PLR
MP

## Slide 23: FRR with RSVP-TE
Typical FRR may provide sub-optimal path
R1
R2
R3
CE1
CE3
R4
R5
R6
CE2
5
n
IGP COST
1
1
5
5
5
1
● Based on circuit concepts
● Sub-optimal Path
● Not ECMP friendly
● Causes link congestion
Primary Path
Expected Backup Path
Actual Backup Path
Link Protection
Configured

## Slide 24: MPLS (Cont.)
Shortcomings:
Doesn’t deal with performance anymore
  CEF, ASIC etc
Requires IGP-LDP synchronization
TE is not scalable
FRR is supported but very difficult to configure and manage
Not suitable for very large carrier network

## Slide 25: SR-MPLS Intro
SR-MPLS 101

## Slide 26: SR-MPLS
LDP+RSVP control plane is complex
SR control plane with IGP
  SR is an extension of IGP
  MPLS is still as the forwarding plane
No LDP, No RSVP-TE are required

## Slide 27: SR-MPLS
R1
R2
R3
R4
CE1
R5
R6
R9
R8
R7
CE2
IP
VPN
16009
IP
VPN
16009
IP
IP
VPN
16009
IP
VPN
16009
IP
VPN
16009
IP
VPN
16009
IP
VPN
PHP
IP
VPN
16009
IP
One of the major ideas behind SR is to keep “Transport Label” consistent “per segment”
PUSH
CONTINUE
NEXT
CE1
CE2

## Slide 28: SR-MPLS
R1
R2
R3
R4
CE1
R5
R6
R9
R8
R7
CE2
IP
VPN
16009
IP
PHP
Traffic is forwarded “Segment by Segment”
16006
16004
IP
VPN
16009
16006
16004
IP
VPN
16009
16006
IP
VPN
16009
16006
IP
VPN
16009
PHP
IP
VPN
16009
IP
VPN
IP
VPN
16009
PHP
IP
“Ordered list of segment” is encapsulated by source node
PUSH
CONTINUE
NEXT

## Slide 29: SR-MPLS
Primary Path
Backup Path
First Segment
Second Segment

## Slide 30: SR-MPLS
Source routing paradigm – SPRING
  SPRING – Source Packet Routing in Networking
  Source node can encapsulate path information using label stack
  Intermediate nodes don’t need to maintain any state
Inserts an “ordered list of segment” with the packet
  A segment is an instruction – topological, service chaining etc
  Segment ID (SID) is equivalent to the LDP Label (in case of SR-MPLS)
  Each SID indicates a segment; the top SID indicates active segment
IGP carries SID information
  No LDP, No RSVP

## Slide 31: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Control Plane
Label generation on each router to reach R4
IGP
IGP
IGP
Index Value: 4
Local Label
16004
Out Label
16004
Local Label
16004
Out Label
16004
Local Label
16004
Out Label
16004
Local Label
1004
Out Label
4004
Local Label
4004
SRGB (all router)
16000 - 23999
In Label = SRGB Base + Originator Node’s SID Index
Out Label = Next-hop’s SRGB Base + Originator Node’s SID Index
Transport (Out) labels are consistent

## Slide 32: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Forwarding Plane
Traffic forwarding from R1 to R4
IP
4004
16004
IGP
IGP
IGP
IP
4004
16004
IP
4004
IP
IP
PHP
BGP Free Core
(RR may require in production)
IP
Transport (Out) labels are consistent
TE and FRR would be easier

## Slide 33: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Control Plane
Label generation on each router to reach R4
IGP
IGP
IGP
Index Value: 4
Local Label
18004
Out Label
19004
Local Label
17004
Out Label
18004
Local Label
16004
Out Label
17004
Local Label
1004
Out Label
4004
Local Label
4004
What if the SRGB is not same on routers
R1: 16000 - 16999
R2: 17000 - 17999
R3: 18000 - 18999
R4: 19000 - 19999
In Label = SRGB Base + Originator Node’s SID Index
Out Label = Next-hop’s SRGB Base + Originator Node’s SID Index
Transport (Out) labels are inconsistent

## Slide 34: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Forwarding Plane
Traffic forwarding from R1 to R4
IP
4004
17004
IGP
IGP
IGP
IP
4004
18004
IP
4004
IP
IP
PHP
BGP Free Core
(RR may require in production)
IP
Transport (Out) labels are inconsistent
TE and FRR would be difficult

## Slide 35: SR-MPLS
Global Segment
Global segments are for routers’ loopback
Assigned from Segment Routing Global Block (SRGB)
  Ranges from 16000 to 23999 for interoperability
  Intended design; highly recommended to keep it same on all router
Keeps transport label consistent per segment (i.e. within IGP domain)
Local Segment
Local segments are for routers’ P2P links
  Assigned from dynamic label range
Supports advanced traffic engineering and FRR
  TE path doesn’t need to be signalled hop-by-hop
Locally significant for the node
But other nodes may need to know it

## Slide 36: SR Control Plane and SID
IGP Segment
Prefix Segment
Node Segment
Anycast Segment
Adjacency Segment
BGP Segment
Prefix Segment
EPE Segment
Peer Node Segment
Peer Adj Segment
Peer Set Segment
IGP Control Plane
BGP Control Plane
OSPF/IS-IS
BGP

## Slide 37: SR Control Plane and SID
R1
R4
R2
R3
Prefix (Node) SID
R1: 16001
Adjacency SID
R1-R2: 24012
Node SID
R3: 16003
Anycast SID
R3: 16023
Adjacency SID
R3-R2: 24032
R3-R4: 24034
Prefix (Node) SID
R4: 16004
Adjacency SID
R4-R2: 24042
R4-R3: 24043
Node SID
R2: 16002
Anycast SID
R2: 16023
Adjacency SID
R2-R1: 24021
R2-R3: 24023
R2-R4: 24024

## Slide 38: SR Control Plane and SID
Node SID: for routers’ loopbacks
  Assigned from SRGB
  Takes IGP shortest path
    Strict shortest path first as a second algorithm (i.e to avoid tunnel in case of autoroute announce)
  Multi-hop
  ECMP Aware
  Should be unique (N=1)
    associated with a single prefix

## Slide 39: SR Control Plane and SID
Anycast SID: for routers’ loopbacks
  Assigned from SRGB
  Takes IGP shortest path
  Multi-hop
  ECMP Aware
  No need to be unique (N=0)
    a SID and IP can be hold by multiple node
  For load-balancing and or redundancy/protection
Adjacency SID: for routers’ P2P links
  Assigned from dynamic range
  To steer traffic via a specific link
  Should be preceded by Node’s Prefix SID

## Slide 40: SR Control Plane and SID
Other IGP SIDs
  Layer-2 Adjacency SID
  Group Adjacency SID
BGP SIDs
  BGP Prefix SID
  BGP Anycast SID
  BGP Peer SID
  BGP Peer Node SID
  BGP Peer Adjacency SID
  …. will be covered later

## Slide 41: SID List
Explicit path can be defined using local segments
Useful for TE and FRR
R1
R4
R2
R3
IP
VPN
16004
24023
16002
CE1
CE2
“Ordered list of segment” is encapsulated by source node
First: Go to R2
Second: go through R2’s Gi0/1
Third: go to R4
Gi0/1
Gi0/2
1
n
IGP COST
1
5
1

## Slide 42: SR-MPLS Features
FRR with TI-LFA
  Avoids micro-looping
Scalable TE
  SR Policy; and no more tunnel
Can be a part of SDN (for inter-domain network)
  PCEP and BGP-LS

## Slide 43: Segment Routing TI-LFA
SR-MPLS Fast Convergence

## Slide 44
Please Note:
● This slide deck is a continuation of previous one “SR-MPLS 101”
● Audience are expected to have prior basic knowledge on MPLS and Segment Routing

## Slide 45: FRR with TI-LFA
Fast Reroute with TI-LFA
Topology Independent LFA
  Sub 50ms convergence time
  Minimizes amount of dropped traffic during convergence
Protects links, nodes and SRLGs
Maintains better SLA

## Slide 46: FRR with TI-LFA
R2
TI-LFA Link Protection
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Topology is fully functional
R1’s Primary path is in forwarding table
1
IP
VPN
16003
“Ordered list of segment” for primary path
10
1

## Slide 47: FRR with TI-LFA
TI-LFA Link Protection
R1 is aware of the backup path in advance in case of link failure to R2
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
1
10
PLR
Protected Link
1

## Slide 48: FRR with TI-LFA
TI-LFA Link Protection
R1 prunes protected link before link failure occurs and find out post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
Protected Link
1

## Slide 49: FRR with TI-LFA
TI-LFA Link Protection
R1 defines the P Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
P Node is such node which can reach source (R1) without using protected link
10
1
P
PLR
Protected Link
1

## Slide 50: FRR with TI-LFA
TI-LFA Link Protection
R1 defines the Q Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Q Node is such node which can reach destination (R3) without using protected link
10
1
Q
PLR
Protected Link
1
P

## Slide 51: FRR with TI-LFA
TI-LFA Link Protection
P Space and Q Space
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
Protected Link
1
Q
P

## Slide 52: FRR with TI-LFA
TI-LFA Link Protection
R1 builds SID-list based on each segment it found along the post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
IP
VPN
16003
24045
16004
Protected Link
“Ordered list of segment” for post convergence path
1
Q
P
Q
P

## Slide 53: FRR with TI-LFA
TI-LFA Link Protection
R1 programs the precomputed SID-List it in forwarding table
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
Protected Link
PLR
IP
VPN
16003
24045
16004
IP
VPN
16003
“Ordered list of segment” for primary path
“Ordered list of segment” for post convergence path
1
Q
P

## Slide 54: FRR with TI-LFA
TI-LFA Link Protection
When protected link goes down R1 instantly use post convergence SID-list even before IGP converges new path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
Protected Link
PLR
Q
P
IP
VPN
16003
24045
16004
“Ordered list of segment” for post convergence path
1

## Slide 55: FRR with TI-LFA
R2
TI-LFA Node Protection
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Topology is fully functional
R1’s Primary path is in forwarding table
1
IP
VPN
16003
“Ordered list of segment” for primary path
10
1

## Slide 56: FRR with TI-LFA
TI-LFA Node Protection
R1 is aware of the backup Node in advance in case of failure of R2
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
1
10
PLR
Protected Node
1

## Slide 57: FRR with TI-LFA
TI-LFA Node Protection
R1 prunes protected node before node failure occurs and find out post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
1
Protected Node

## Slide 58: FRR with TI-LFA
TI-LFA Node Protection
R1 defines the P Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
P Node is such node which can reach source (R1) without using protected node
10
1
P
PLR
1
Protected Node

## Slide 59: FRR with TI-LFA
TI-LFA Node Protection
R1 defines the Q Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Q Node is such node which can reach destination (R3) without using protected node
10
1
Q
PLR
1
P
Protected Node

## Slide 60: FRR with TI-LFA
TI-LFA Node Protection
P Space and Q Space
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
1
Q
P
Protected Node

## Slide 61: FRR with TI-LFA
TI-LFA Node Protection
R1 builds SID-list based on each segment it found along the post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
IP
VPN
16003
24056
24045
“Ordered list of segment” for post convergence path
1
P
Protected Node
Q
16004

## Slide 62: FRR with TI-LFA
TI-LFA Node Protection
R1 programs the precomputed SID-List it in forwarding table
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
IP
VPN
16003
“Ordered list of segment” for primary path
“Ordered list of segment” for post convergence path
1
Protected Node
P
Q
IP
VPN
16003
24056
24045
16004

## Slide 63: FRR with TI-LFA
TI-LFA Node Protection
When protected node goes down R1 instantly use post convergence SID-list even before IGP converges new path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
“Ordered list of segment” for post convergence path
1
Protected Node
P
Q
IP
VPN
16003
24056
24045
16004

## Slide 64: FRR with TI-LFA
Fast Reroute with TI-LFA
SR must be implemented to have TI-LFA
100% topology coverage
Avoids micro-loop
ECMP friendly
Protects IP and LDP traffic also

## Slide 65: TI-LFA: Few more…
SR-MPLS Fast Convergence

## Slide 66: FRR Conditions
LFA Condition
Distance (N, D) < Distance (N, PLR) + Distance (PLR, D)
Case 1:
R1
R2
R3
R4
R5
1
1
1
2
Primary Next-hop
Backup Next-hop
1
R6
1
CE1
CE2
R5 is a LFA
for R1
N = LFA Candidate
D = Destination Node
PLR = Point of Local Repair

## Slide 67: FRR Conditions
LFA Condition
Distance (N, D) < Distance (N, PLR) + Distance (PLR, D)
Case 2:
R1
R2
R3
R4
R5
1
1
1
1
Primary Next-hop
Not a
Backup Next-hop
1
R6
2
CE1
CE2
R5 is not a LFA
for R1
N = LFA Candidate
D = Destination Node
PLR = Point of Local Repair

## Slide 68: FRR Conditions
LFA Condition
Distance (N, D) < Distance (N, PLR) + Distance (PLR, D)
Case 3:
R1
R2
R3
R4
R5
1
1
1
1
Primary Next-hop
Not a
Backup Next-hop
1
R6
1
CE1
CE2
R5 is not a LFA
for R1
N = LFA Candidate
D = Destination Node
PLR = Point of Local Repair

## Slide 69: FRR Conditions
RLFA Condition
  P node: Closest Node to PLR whose backup path is not via protected link
  Q node: Closest Node to DESTINATION whose backup path is not via protected link
  A PQ node can be used as RLFA
  Case 1:
R1
R2
R3
R4
R5
1
1
1
1
Primary Next-hop
Not a
Backup Next-hop
1
R6
2
CE1
CE2
R6 is a RLFA
for R1
Q
P
Ex-P
Q
Q

## Slide 70: FRR Conditions
RLFA Condition
  P node: Closest Node to PLR whose backup path is not via protected link
  Q node: Closest Node to DESTINATION whose backup path is not via protected link
  A PQ node can be used as RLFA
  Case 2:
R1
R2
R3
R4
R5
2
1
1
1
Primary Next-hop
Not a
Backup Next-hop
1
R6
1
CE1
CE2
R6 is not a RLFA
for R1
Q
P
Q
Q

## Slide 71: TI-LFA Protection
R1
R2
R3
CE1
CE3
R4
R5
R6
CE2
5
n
IGP COST
1
1
5
5
5
1
Primary Path
Backup Path
Link Protection
Configured
Destination (Prefix) based FRR; not based on links
  Results in more optimized path

## Slide 72: TI-LFA Protection
Link protection sometimes can protect the node also
Node protection can always protect the link
Case: 1
R1
R2
R3
CE1
CE2
R4
Link Protection
Configured
Also protects the node
1
1
1
1

## Slide 73: TI-LFA Protection
Link protection sometimes can protect the node also
Node protection can always protect the link
Case: 2
R1
R2
R3
CE1
CE2
R4
Node Protection
Configured
Also protects the link
1
1
1
1

## Slide 74: TI-LFA Protection
A bigger picture…
R1
R5
R8
CE1
CE2
R2
R3
R7
R6
Domain 1
Domain 2
RR
RR
SR PCE
BGP-LS
BGP-LS
BGP-LS
PCEP
R4
Regular Path
Repaired Path by FRR
New Path Signaled by PCE

## Slide 75: Microloop
Microloop: Transient packet forwarding loop during path convergence
Reasons of Microloop:
  Topological change propagation may need few times
  Forwarding table may not be updated at the same time or in a proper order
  Depends on CPU, memory and link utilization also
  Intermittent link flapping
R1
R2
R3
CE1
CE2
R4
Microloop
1
1
1
5

## Slide 76: Microloop
Without TI-LFA
  Causes packet loss due to microloop
R1
R2
R3
CE1
CE2
R4
Microloop
1
1
1
5
0 ms
200 ms
400 ms
Link R1-R2 goes down
R1 updates forwarding table
R4 updates forwarding table
Traffic dropped by R1
Microloop between R1 and R4
Path is converged

## Slide 77: Microloop
With TI-LFA; but no microloop avoidance enabled
  Much faster convergence but still microloop is there
R1
R2
R3
CE1
CE2
R4
Microloop
1
1
1
5
0 ms
40 ms
200 ms
Link R1-R2 goes down
R1 activates TI-LFA
R1 updates forwarding table
And removes TI-LFA path
Traffic dropped by R1
R1 forwards traffic via repair path
400 ms
R4 updates forwarding table
Microloop between R1 and R4
Path is converged and R1 deactivates TI-LFA
IP
VPN
16003
24043
16004
Backup SID-List

## Slide 78: Microloop Avoidance
With TI-LFA; and microloop avoidance enabled
  Much faster convergence and no microloop is there
R1
R2
R3
CE1
CE2
R4
Microloop
1
1
1
5
0 ms
40 ms
400 ms
Link R1-R2 goes down
R1 activates TI-LFA
R4 updates forwarding table
Traffic dropped by R1
R1 forwards traffic via repair path
5000 ms
R1 updates forwarding table
And removes TI-LFA path
Traffic forwarded via repair path (Continued)
Path is converged and R1 deactivates TI-LFA
Microloop avoidance feature enables R1
to update its forwarding table later;
to let other routers to update themselves first

## Slide 79: TI-LFA Load Balancing
Prefix-SID is ECMP aware
PLR can load balance over multiple PQ pairs
  Selects one PQ pair per destination (based on hash function)
R1
R2
R3
CE1
CE2
R7
1
1
1
1
R8
R9
R4
R5
R6
8
4
1
4
8
1
Q
P
PLR
P
Q
IP
VPN
16003
24045
16004
Backup SID-List
1
IP
VPN
16003
24078
16007
Backup SID-List
2
Case 1:

## Slide 80: TI-LFA Load Balancing
Prefix-SID is ECMP aware
PLR can load balance over multiple PQ pairs
  Selects one PQ pair per destination (based on hash function)
R1
R2
R3
CE1
CE2
1
1
1
R8
R9
R4
R5
R6
8
4
1
4
8
1
Q
P
PLR
Q
IP
VPN
16003
24045
16004
Backup SID-List
1
IP
VPN
16003
24048
16004
Backup SID-List
2
Case 2:

## Slide 81: TI-LFA Load Balancing
Prefix-SID is ECMP aware
PLR can load balance over multiple PQ pairs
  Selects one PQ pair per destination (based on hash function)
R1
R2
R3
CE1
CE2
1
1
1
R4
R5
R6
8
4
8
1
Q
P
PLR
IP
VPN
16003
24045
16004
Backup SID-List
1
IP
VPN
16003
24075
16007
Backup SID-List
2
Case 3:
R7
P
1

## Slide 82: Lab - Demo of Microloop Prevention and Load Balancing
SR-MPLS Fast Convergence

## Slide 83: Lab - Demo of TI-LFA FRR vs RSVP FRR
SR-MPLS Fast Convergence

## Slide 84: Segment Routing TE (SR-TE)
SR-MPLS Traffic Engineering

## Slide 85
Please Note:
● This slide deck is a continuation of previous one “SR-MPLS 101”
● Audience are expected to have prior basic knowledge on MPLS and Segment Routing

## Slide 86: SR-TE
Segment Routing Traffic Engineering
To steer traffic through longer path
SR Policy to be implemented at ingress PE
  No more tunnel from head-end to tail-end
No state to be maintained at intermediate nodes
  No RSVP-TE means no additional signalling
Supports built-in FRR with TI-LFA
ECMP friendly

## Slide 87: SR-TE
Segment Routing Traffic Engineering
SR Policy
  Intended design
  Highly scalable
  Better optimization
  Automated traffic steering
Can be applied in either centralized or distributed manner
  Explicit Path: CLI or SDN Controller
  Dynamic Path: Based on constrain (i.e link delay)

## Slide 88: SR-TE
RSVP-TE
R2
R1
R3
R4
CE1
R5
CE2
CE1
CE2
PATH
PATH
PATH
PATH
PATH
PATH
PATH
PATH
RESV
RESV
RESV
RESV
RESV
RESV
R1 and R2 require to maintain two separate states for two tunnels
RSVP-TE Tunnel 1
R1 > R2 > R4 > R3
RSVP-TE Tunnel 2
R1 > R2 > R5 > R3

## Slide 89: SR-TE
SR-TE
R2
R1
R3
R4
CE1
R5
CE2
CE1
CE2
No tunnel required
SR Policy 1
R1 > R2 > R4 > R3
SR Policy 2
R1 > R2 > R5 > R3

## Slide 90: SR-TE
SR-TE
R2
R1
R3
R4
CE1
R5
CE2
CE1
CE2
SID-List will be imposed at
source node based on SR Policy
SR Policy 1
R1 > R2 > R4 > R3
SR Policy 2
R1 > R2 > R5 > R3
IP
VPN
16003
16005
16002
IP
VPN
16003
16004
16002
Intermediary nodes don’t need to do anything extra

## Slide 91: SR-TE
SR Policy
  headend, color, endpoint
R2
R1
R3
R4
Color is used to express the intent
Color must be unique between a pair of headend and endpoint
Color is originally a numeric value
R5
CE1
CE2
CE1
CE2
R1, Pink, R3
R1, Green, R3

## Slide 92: SR Policy
SR-MPLS Traffic Engineering

## Slide 93: SR Policy
SR Policy: Configuration example
segment-routing
traffic-eng
policy POLICY1 Policy Name
color 10 end-point ipv4 10.1.1.3 End-point
candidate-paths Color value
preference 100 Path Preference
explicit segment-list SID-LIST1 Path Name
segment-list name SID-LIST1
index 10 mpls label 16002 Node/Link to follow
index 20 mpls label 24023
index 30 mpls label 16004 Path Sequence

## Slide 94: SR Policy
A SR Policy is consisting of “headend, color, endpoint”
R2
R1
R3
R4
R5
CE1
CE2
CE1
CE2
R1, Pink, R3
R1, Green, R3
policy POLICY1
color 10 end-point ipv4 10.1.1.3
policy POLICY2
color 20 end-point ipv4 10.1.1.3

## Slide 95: SR Policy
Color is an intent or business requirements
  Shortest Path, Minimum Delay, To avoid any link/node, Automated traffic steering etc
Color is a numeric value and must be unique per H, E pair
R2
R1
R3
R4
R5
CE1
CE2
CE1
CE2
R1, Pink, R3
R1, Green, R3

## Slide 96: SR Policy
Candidate Path
  SR policy contains one or more Candidate Path (cPath)
  cPath has a preference value
    Higher value is preferred; Not based on any protocol priority
  cPath can be configure by CLI or PCE or dynamically
policy POLICY1
color 10 end-point ipv4 10.1.1.3
candidate-paths
preference 100
explicit segment-list SID-LIST1
preference 150
explicit segment-list SID-LIST2
cPath 1
cPath 2

## Slide 97: SR Policy
Candidate Path
  Multiple SID-LIST can be configured using weight value
  Weight is used to load share the traffic
cPath 2
cPath 1
policy POLICY1
color 10 end-point ipv4 10.1.1.3
candidate-paths
preference 100
explicit segment-list SID-LIST1
preference 150
explicit segment-list SID-LIST2
weight 4
explicit segment-list SID-LIST3
weight 1

## Slide 98: SR Policy
Candidate Path
  Multiple cPath can be source of an active path; and programmed in forwarding table
  A path must be valid to be an active path
    Tie-breaker also available in case of multiple active path
cPath 2
cPath 1
cPath 3
Valid
Invalid
Invalid
Invalid
Active Path
policy POLICY1
color 10 end-point ipv4 10.1.1.3
candidate-paths
preference 100
explicit segment-list SID-LIST1
preference 150
explicit segment-list SID-LIST2
weight 4
explicit segment-list SID-LIST3
weight 1
preference 200
explicit segment-list SID-LIST4
Let’s assume

## Slide 99: SR Policy
Explicit cPath
  Configured by CLI or PCE
Dynamic cPath
  Configured dynamically based on link attributes (like low delay)
  SR Native Algorithm to translate intent to SID-LIST
policy POLICY1
color 10 end-point ipv4 10.1.1.3
candidate-paths
preference 100
explicit segment-list SID-LIST1
preference 150
dynamic
metric
type delay
cPath 2
(Dynamic)
cPath 1 (Explicit)

## Slide 100: SR Policy
Explicit cPath can be configured:
  By defining SID (MPLS Label)
  By defining Segment Descriptor (Prefix or Adjacency)
Headend needs to validate SID-LIST before using it
segment-list name SID-LIST1
index 10 mpls label 16002
index 20 mpls label 24023
index 30 mpls label 16004
segment-list name SID-LIST2
index 10 address ipv4 10.1.1.2
index 20 address ipv4 10.1.23.2
index 30 address ipv4 10.1.1.4
SID-LIST2
SID-LIST1

## Slide 101: SR Policy
Dynamic cPath can be configured:
  By headend or by PCE
    By defining SID (MPLS Label), or by defining Segment Descriptor (Prefix or Adjacency)
  Path re-computed automatically
May have optimization objectives
  Minimum metric or delay
May have set of constraints
  Maximum cumulative metric, delay or other constraints

## Slide 102: SR Policy
Dynamic cPath
  Database contains all information
    Headend's SR-TE DB may contain info of the local domain only
    PCE’s SR-TE DB contains info of all domains
  Computation Engine to compute optimized path
    Translate intents into SID-List
    Distributed computation
    Centralized computation
  Headend and PCE use same algorithm
    SR Native Algorithm

## Slide 103: SR Policy
Dynamic cPath Distributed Computation
  Done by headend router
  Headend may contain low delay path
    Flooded by IGP
    Stored in SR-TE-DB
Dynamic cPath Centralized Computation
  Done by PCE
  PCE collects info from PCC (headend) using BGP-LS
  PCC requests for path info (based on optimization objectives and constraints)
    Path Request, Reply and Report
  PCE sends path to PCC in the form of a SID-List
  PCC can delegate the path option to PCE

## Slide 104: SR Policy
Some use cases:
SID-List
  Controller based multi domain network
    Doesn’t have full visibility at headend
  No need multiple resolve
Segment Descriptor
  In case of full visibility
  Operator may need headend monitoring
  Dynamic labels (Adj-SID) are difficult to guess
    Exception: Adj-SID, Peering SID can also be configured manually

## Slide 105: SR Policy
Binding SID (BSID)
  BSID is the identifier of a SR Policy
  Configured automatically; or can be configured manually
  Can be used as In Label in multi-domain network
policy POLICY1
color 10 end-point ipv4 10.1.1.3
binding-sid mpls 40001
candidate-paths
preference 100
explicit segment-list SID-LIST1
preference 150
explicit segment-list SID-LIST2
BSID

## Slide 106: SR Policy
Domain 2 - SR
Binding SID (BSID)
  BSID is the identifier of a SR Policy
  Configured automatically; or can be configured manually
  Can be used as In Label in multi-domain network
R2
R1
R3
R4
R5
CE1
CE2
CE1
CE2
R1, Pink, R3
R1, Green, R3
Rn
IP
VPN
40001
IP
VPN
40002
Domain 1 - LDP/SR

## Slide 107: Constraints
Constraints based TE
Constraints can be:
  Include and/or exclude TE Affinity
  Include and/or exclude IP Address
  Include and/or exclude SRLG
    Shared Link Resource Group
  Maximum accumulated metric
    IGP, TE, Delay
  Maximum number of SID in the SID-LIST
  Disjoint path from another SR Policy

## Slide 108: Constraints
R1, Pink, R3
Path: R1 > R4 > R5 > R3
Exclude: R4-R5 (Upper Link)
R1, Green, R3
Path: R1 > R6 > R7 > R3
Exclude: Node R4
Link / Node Exclusion
R2
R1
R3
CE1
CE2
CE1
CE2
R4
R5
R6
R7
1
n
TE COST
1
1
1
1
2
5
1
1
2
1
1
1
5
1
n
IGP COST
5
5
1

## Slide 109: Constraints
Link Exclusion
#R1#
policy POLICY1
color 10 end-point ipv4 10.1.1.3
candidate-paths
preference 100
dynamic
metric type te
constraints
affinity
exclude-any color PINK
#All Router#
router ospf 1
distribute link-state
#R1, R4#
segment-routing
traffic-eng
affinity-map
color PINK bit-position 0
#R4#
interface gi0/0/0/1
affinity color PINK
R1, Pink, R3
Path: R1 > R4 > R5 > R3
Exclude: R4-R5 (Upper Link)

## Slide 110: Constraints
Node Exclusion
#R1#
policy POLICY2
color 20 end-point ipv4 10.1.1.3
candidate-paths
preference 100
dynamic
metric type te
constraints
address
exclude PSET1
#R1#
prefix-set PSET1
10.1.1.4
end-set
R1, Green, R3
Path: R1 > R6 > R7 > R3
Exclude: Node R4

## Slide 111: Constraints
SRLG Exclusion
  SRLG means multiple links share same resource
  i.e. Fiber path, conduit, patch panel etc
R1, Pink, R3
Path: R1 > R6 > R7 > R3
Exclude: R4 SRLG
R2
R1
R3
CE1
CE2
CE1
CE2
R4
R5
R6
R7
1
n
TE COST
1
1
1
1
2
5
1
1
2
1
1
1
5
1
n
IGP COST
5
5
1

## Slide 112: Constraints
SRLG Exclusion
  Shared Link Resource Group
#R1#
policy POLICY1
color 10 end-point ipv4 10.1.1.3
candidate-paths
preference 100
dynamic
metric type te
constraints
srlg
exclude 1111
#R4#
srlg
interface gi0/0/0/1
10 value 1111
interface gi0/0/0/1
10 value 1111
R1, Pink, R3
Path: R1 > R6 > R7 > R3
Exclude: R4 SRLG

## Slide 113: Constraints
Disjoint Path
  SR-TE can compute a path which is disjoint from another path in same disjoint-group
  Link, Node, SRLG
  Plain A, Plain B etc
    Avoid congestion, maintaining SLA, Load balancing etc.
R2
R6
R1
R5
R4
R8
R3
R7
CE1
CE2
CE1
CE2
R9
R10

## Slide 114: Path Validation
Explicit Path
SID-List must be validated:
  Should have at least one SID
  Weight should be larger than 0
    default is 1
  Headend to resolve IPs in exp-path in to MPLS labels
  Headend to resolve first SID to find out reachable next-hop
  Any constraints can be considered (optional)
If any intermediary link fails:
  Adj-SID is withdrawn
  Corresponding node will perform TI-LFA
    For around 15 minutes at maximum

## Slide 115: Path Validation
Dynamic Path
SID-List must be validated:
  Should have at least one SID
  Weight should be larger than 0
    default is 1
  Headend to resolve IPs in exp-path in to MPLS labels
  Headend to resolve first SID to find out reachable next-hop
  Any constraints can be considered (optional)
If any intermediary link fails:
  Adj-SID is withdrawn
  Corresponding node will perform TI-LFA
    For around 15 minutes at maximum

## Slide 116: Traffic Steering
Auto Route
  IGP steers all the traffic towards destination and other downstream nodes
  Localized behaviour on headend
R1, Pink, R3
Path: R1 > R4 > R5 > R6 > R3
R2
R1
R3
CE1
CE2
CE1
CE2
R4
R6
R5
R7
R1, Green, R7
NO POLICY CONFIGURED !!

## Slide 117: Traffic Steering
Auto Route
  Limited to local IGP area
  Limited to per-BGP next-hop
  Steers all service traffic destined for BGP next-hop
Policy Based Routing
  Can steer traffic for any specific VPN, or PW
Static Route
  Requires static route to specified next-hop for individual services
Anything better than these?
  Automated Steering

## Slide 118: Lab - Demo of SR Policy
SR-MPLS Traffic Engineering

## Slide 119: SRGB: Few more…
Segment Routing Global Block

## Slide 120: SRGB
SRGB serves Node SID and Anycast SID
SRGB Size > Number of Node
SRGB range/size should be identical on all node
Different platforms maybe different capacity of total number of SIDs
Modification of SRGB range may disrupt traffic
  A reboot may require
Label range:
  0 to 15: Special Purpose Label
  16 to 15999: Static MPLS Label
  16000 to 23999: Default SRGB Label
  24000 to 2^20-1: Dynamic Label

## Slide 121: SR and LDP Coexistence
SR-MPLS

## Slide 122: SR and LDP
SRGB serves Node SID and Anycast SID
SRGB Size > Number of Node
SRGB range/size should be identical on all node
Different platforms maybe different capacity of total number of SIDs
Modification of SRGB range may disrupt traffic
  A reboot may require
Label range:
  0 to 15: Special Purpose Label
  16 to 15999: Static MPLS Label
  16000 to 23999: Default SRGB Label
  24000 to 2^20-1: Dynamic Label

## Slide 123: Thank you!