## Slide 1: BGP Route Reflector
Design Guideline
M Abdullah Al Naser
Datacom Professional
mnaser.net@gmail.com
Version 0.1

## Slide 2
Pre-requisite:
Participants are expected to have prior knowledge in IP routing, preferably on OSPF and BGP.

## Slide 3: BGP Recap
BGP Route Reflector

## Slide 4: BGP Recap
BGP is a path-vector routing protocol
  Intended for internet routing

## Slide 5: BGP Recap
BGP has two variations
  eBGP
    To peer with BGP speakers reside in different AS
  iBGP
    To peer with BGP speakers reside in same AS
BR
R3
R1
R2
Internet
eBGP
iBGP
iBGP
iBGP

## Slide 6: BGP Recap
Why iBGP if IGP still exists?
  (i)BGP is to deal with large number of internet prefix
Then why IGP if iBGP is there?
  For quick next-hop resolution
  Stabilizes iBGP sessions
BR
R3
R1
R2
Internet
eBGP
iBGP
iBGP
iBGP
OSPF

## Slide 7: BGP Recap
A BGP speaker receives prefixes from eBGP peer and sends it to iBGP peer
A BGP speaker receives prefixes from iBGP peer and sends it to eBGP peer but doesn’t send it to other iBGP peer
BR
R3
R1
R2
Internet
eBGP
iBGP
iBGP
iBGP

## Slide 8: BGP Recap
A BGP speaker receives prefixes from eBGP peer and sends it to iBGP peer
A BGP speaker receives prefixes from iBGP peer and sends it to eBGP peer but doesn’t send it to other iBGP peer
Why?
  Split horizon rule
  To prevent loop
BR
R3
R1
R2
Internet
eBGP
iBGP
iBGP
iBGP

## Slide 9: BGP Loop Prevention
Router checks AS-PATH for prefixes received from eBGP peer
  If own ASN is found in AS-PATH, then prefixes are discarded
Prefixes originated by a router and sent to iBGP peers don’t have any AS-PATH set
  Difficult from other iBGP routers to determine any possible loop
So, a plain and simple solution: don’t send it to other iBGP peer
Any solution to this problem?
BR
R3
R1
R2
Internet
eBGP
iBGP
iBGP
iBGP

## Slide 10: iBGP Peering
iBGP requires one to one peering among speakers
  Popularly known as full mesh peering
  IGP helps to make sure loopbacks are reachable
Number of peering = n(n-1)/2
  4*(4-1)/2 = 6
BR
R3
R1
R2
Internet
iBGP
iBGP
iBGP
iBGP
iBGP
iBGP

## Slide 11: iBGP Peering
What if number of routers are huge in the network?
  Full mesh adds configuration overhead
  Requires good amount of resources
  Not scalable
Any solution to this problem?
BR
R3
R1
R2
Internet
R4
R5
R6
R7

## Slide 12: BGP Route Reflector
Routers need to form iBGP peering with the Route Reflector (RR) only
  Eliminates full mesh peering
  Saves life
RR receiving routing update from one iBGP peer reflects to…
  other iBGP peers
    client and non-client
BR
R3
R1
R2
Internet
R4
R5
R6
R7
RR

## Slide 13: RR Advertisement
Route advertised by RR
Received from eBGP peer
  Sends to all client and non-client
Received from RR client
  Sends to all eBGP peer
  Reflects to client and non-client
Received from RR non-client
  Sends to all eBGP peer
  Reflects to all client
  Doesn’t reflect to any non-client
Non-clients are required to peer separately
RR
R3
R1
R2
Internet
R4
R5
Client
Client
Non-Client
Non-Client
Client
iBGP

## Slide 14: BGP Next-hop
A mandatory BGP attribute
Router changes next-hop for prefixes
  Received from eBGP and send to eBGP
Router doesn’t change next-hop for prefixes
  Received from eBGP and send to iBGP
  Prefixes with external NH is still unreachable
    Propagating external NH into IGP doesn’t always sound good
R2
R4
R3
eBGP
R1
10.0.0.0/24
10.0.0.0/24
NH: R1
eBGP
10.0.0.0/24
NH: R2
10.0.0.0/24
NH: R1
iBGP
R2 doesn’t
change NH
R2
changes
NH

## Slide 15: BGP Next-hop
A mandatory BGP attribute
Router changes next-hop for prefixes
  Received from eBGP and send to eBGP
Router doesn’t change next-hop for prefixes
  Received from eBGP and send to iBGP
  Prefixes with external NH is still unreachable
    Propagating external NH into IGP doesn’t always sound good
A good idea is to forcibly change NH
  for iBGP peers only
R2
R4
R3
eBGP
R1
10.0.0.0/24
10.0.0.0/24
NH: R1
eBGP
10.0.0.0/24
NH: R2
10.0.0.0/24
NH: R2
iBGP
R2 change NH
R2
changes
NH
Next-hop Self

## Slide 16: BGP Next-hop
Does RR change Next-hop?
  Answer: NO (by default)
Next-hop should be reachable via IGP
Traffic is forwarded via IGP shortest path
RR
R3
R1
R2
10.0.0.0/24
10.0.0.0/24
NH: R1
10.0.0.0/24
NH: R1
Physical Link
iBGP Peering
Prefix Flow
Traffic Flow

## Slide 17: BGP Next-hop
RR may or may not forward traffic
  Depends on whether RR is in traffic path or not
Dedicated RR is preferred for larger networks
R0
R3
R1
R2
10.0.0.0/24
10.0.0.0/24
NH: R1
10.0.0.0/24
NH: R1
RR
R3
R1
R2
10.0.0.0/24
10.0.0.0/24
NH: R1
10.0.0.0/24
NH: R1
RR in traffic path
(Inline RR)
RR
RR not in traffic path
(Dedicated RR)
Physical Link
iBGP Peering
Prefix Flow
Traffic Flow
10.0.0.0/24
NH: R1

## Slide 18: RR Redundancy
How many RR do we need in production network?
  At least two
  For redundancy
Each client to be peer with multiple RR
Does it contribute to any loop?
  Answer: It depends
Does RRs need to peered in between?
  Answer: It depends
Let’s discuss it!
R3
R1
R2
RR1
RR2
R4

## Slide 19: RR Loop Prevention
How does RR prevent route loop?
  Originator ID
    RR adds Originator ID with the prefix received from client
    Originator ID is added in BGP path information
    Originator ID is the BGP router-id of client
    Router checks the Originator ID of the prefix received from RR
    Router discards prefix if Originator ID matches with own BGP router-id
R3
R1
R2
RR1
RR2
R4
Router-id
10.1.1.1
Network
10.0.0.0/24
10.0.0.0/24
Originator ID: 10.1.1.1

## Slide 20: RR Loop Prevention
How does RR prevent route loop?
  Cluster List
    Each RR should be configured with a Cluster ID
    Cluster ID can be manually configured or derived from the BGP router-id of RR itself
    Cluster ID helps to form a Cluster List
    Cluster List may contain one or more Cluster ID (depending on how many RRs are in the path)
    Cluster List is added in BGP path information
    Router (RR) discards prefix if it finds its own Cluster ID in the Cluster List
R3
R1
R2
RR1
RR2
R4
Cluster ID
10.1.1.10
Network
10.0.0.0/24
10.0.0.0/24
Cluster List:
10.1.1.10
Cluster ID
10.1.1.20
10.0.0.0/24
Cluster List:
10.1.1.20,
10.1.1.30,
10.1.1.10
RR3
Cluster ID
10.1.1.30
10.0.0.0/24
Cluster List:
10.1.1.30,
10.1.1.10

## Slide 21: RR Loop Prevention
Should we configure same or different Cluster ID on all RRs?
  It depends on requirements
    Are RRs for only redundancy? Then same Cluster ID can be configured
    Are RRs for load sharing? Then different Cluster ID should be configured
R3
R1
R2
RR1
RR2
R4
Cluster ID
10.1.1.10
Cluster ID
10.1.1.10
Two RRs in same cluster
For RR Redundancy Only
Caution: Route might get lost if R1 and R2 loss peering with RR1 and RR2 respectively
Physical links and IGP path should be designed carefully

## Slide 22: RR Loop Prevention
Should we configure same or different Cluster ID on all RRs?
  It depends on requirements
    Are RRs for only redundancy? Then same Cluster ID can be configured
    Are RRs for load sharing? Then different Cluster ID should be configured
R3
R1
R2
RR1
RR2
R4
Cluster ID
10.1.1.10
Cluster ID
10.1.1.10
Two RRs in same cluster
For RR Redundancy Only
Caution: Route might get lost if R1 and R2 loss peering with RR1 and RR2 respectively
Physical links and IGP path should be designed carefully
R2 can’t have R1’s route and vice versa

## Slide 23: RR Loop Prevention
Should we configure same or different Cluster ID on all RRs?
  It depends on requirements
    Are RRs for only redundancy? Then same Cluster ID can be configured
    Are RRs for load sharing? Then different Cluster ID should be configured
R3
R1
R2
RR1
RR2
R4
Cluster ID
10.1.1.10
Cluster ID
10.1.1.20
Two RRs in two different cluster
R3
R1
R2
RR1
RR2
R4
Cluster ID
10.1.1.10
Cluster ID
10.1.1.20
Two RRs in two different cluster
RR Load Sharing
RR Load Sharing and Redundancy

## Slide 24: RR Loop Prevention
Should we configure same or different Cluster ID on all RRs?
  It depends on requirements
    Are RRs for only redundancy? Then same Cluster ID can be configured
    Are RRs for load sharing? Then different Cluster ID should be configured
R3
R1
R2
RR1
RR2
R4
Cluster ID
10.1.1.10
Cluster ID
10.1.1.20
Two RRs in two different cluster
RR Load Sharing and Redundancy
From which RR, R2 should receive R1’s route?
  Answer: RR1
  Hints: Lowest BGP neighbor router-id

## Slide 25: RR Loop Prevention
Should we configure same or different Cluster ID on all RRs?
  It depends on requirements
    Are RRs for only redundancy? Then same Cluster ID can be configured
    Are RRs for load sharing? Then different Cluster ID should be configured
R3
R1
R2
RR1
RR2
R4
Cluster ID
10.1.1.10
Cluster ID
10.1.1.20
Two RRs in two different cluster
RR Load Sharing and Redundancy
From which RR, R2 should receive R1’s route?
  Answer: RR1
  Hints: Shortest Cluster List
  Cluster List from RR1: 10.1.1.10
  Cluster List from RR2: 10.1.1.10, 10.1.1.20

## Slide 26: Hierarchical RR Design

## Slide 27: Thank you!