## Slide 1: MPLS Traffic Engineering
RSVP-TE
M Abdullah Al Naser
Datacom Professional
mnaser.net@gmail.com
Version 0.1

## Slide 2: MPLS TE 101
MPLS TE

## Slide 3: MPLS TE
MPLS Protocols
  Label Distribution Protocol (LDP)
  Border Gateway Protocol (BGP)
  Resource Reservation Protocol for TE (RSVP-TE)
  Segment Routing (SR); an IGP extension
All these protocols require an IGP to work
  Open Shortest Path First (OSPF)
  Integrated Intermediate System to Intermediate System (IS-IS)
MPLS TE: to steer traffic through longer path
  To utilize unused links
  To avoid congestion on busy links
IGP always takes the shortest path

## Slide 4: MPLS-TE
RSVP, originally invented for IP QoS
  Replaced by IP Precedence and DSCP
RSVP-TE is an extension of legacy RSVP
  A signalling protocol for MPLS TE
RSVP-TE builds a new LSP between two PEs
  LSPs are unidirectional

## Slide 5: RSVP-TE
Creates circuits; state is signalled hop-by-hop
Need to configure link constraints (BW and other attributes)
Distribute TE info using IGP extension
PCALC (CSPF) to calculate best path
Carries TE labels to signal tunnel from head-end to tail-end PE
Push traffic into the tunnel
  Manual, Auto-route
  Tunnel fallback provides less traffic disruption

## Slide 6: RSVP-TE
Shortest Path
R1
R2
R3
R4
CE1
CE2
Control Plane
RSVP PATH messages reserve BW and request for MPLS label
R5
PATH
PATH
PATH
PATH
Head-end
Tail-end

## Slide 7: RSVP-TE
Shortest Path
R1
R2
R3
R4
CE1
CE2
Control Plane
RSVP RESV messages carry MPLS label
RESV
RESV
RESV
TE
Path
RESV
TE PATH is signaled “hop-by-hop” based on ERO !!!
R5
PATH
PATH
PATH
PATH
Head-end
Tail-end

## Slide 8: RSVP-TE
Shortcomings:
Tunnel is not bidirectional
IGP tracks link constraints and floods periodically
  Maintains state
  TE tunnel need to be re-optimized frequently
RSVP-TE isn’t ECMP friendly (N2*K tunnel required)
  Doesn’t scale well with inter-domain (IGP) network
Additional overhead for
both router and it’s administrator
Why is RSVP-TE still useful?

## Slide 9: RSVP-TE
MPLS TE

## Slide 10: RSVP-TE
RSVP-TE Link Information
Total available BW of interface
Maximum Reservable BW of interface
TE metric
Link affinity (attribute flags)
SRLG
Supporting IGPs
OSPF Opaque LSA (Type 10)
IS-IS TLV/Sub-TLV

## Slide 11: RSVP-TE
RSVP-TE Messages
Path
Resv
PathErr
ResvErr
PathTear
ResvTear

## Slide 12: RSVP-TE
RSVP-TE Objects
Label Request
Label
Explicit_Route
Record_Route
Session_Attribute

## Slide 13: RSVP-TE
IGP info is flooded within the area
  Info stored in TE database
  TED is not a LSDB
Runs CSPF with one or more constraints
  Different from regular SPF algorithm
  Constraints can be:
    BW requirement of tunnel
    Available BW of interface
    Explicit_Route
    Setup priority and holding priority
    Link color (Administrative groups)

## Slide 14: RSVP-TE
Path Setup
Path setup requires a signalling protocol
  RSVP-TE
Path setup functions
  Path setup and maintenance
  Path teardown
  Error signalling

## Slide 15: RSVP-TE
Path Setup
R1
R2
R3
R4
CE1
CE2
RESV
RESV
RESV
TE
Path
RESV
R5
PATH
PATH
PATH
PATH
Head-end
Tail-end

## Slide 16: RSVP-TE
Pushing traffic through the tunnel
Static route
Policy based route (PBR)
Autoroute announce
Auto route destination
Forwarding adjacency
Policy-based tunnel selection
Class-based tunnel selection

## Slide 17: MPLS TE
MP-BGP
R1
R2
R3
R4
CE1
CE2
Control Plane
Label generation on each router to reach R4
IGP
IGP
IGP
Index Value: 4
Local Label
16004
Out Label
16004
Local Label
16004
Out Label
16004
Local Label
16004
Out Label
16004
Local Label
1004
Out Label
4004
Local Label
4004
SRGB (all router)
16000 - 23999
In Label = SRGB Base + Originator Node’s SID Index
Out Label = Next-hop’s SRGB Base + Originator Node’s SID Index
Transport (Out) labels are consistent

## Slide 18: Lab - Demo of SR Policy
SR-MPLS Traffic Engineering

## Slide 19: Thank you!