## Slide 1: Segment Routing Control Plane
IGP and BGP Control Plane
Version 0.1

## Slide 2
Please Note:
● This slide deck is a continuation of previous one “SR-MPLS 101”
● Few slides may overlap to recap some basic SR stuffs
● Audience are expected to have prior basic knowledge on MPLS and Segment Routing

## Slide 3: IGP Control Plane
Segment Routing Control Plane

## Slide 4: SR IGP Control Plane
IGP has been extended for SR capability
  OSPFv2: Supports SR for IPv4 (Multi area)
  OSPFv3: Supports SR for IPv6 for both SR-MPLS and SRv6)
  IS-IS: Supports SR for IPv4 and IPv6 (Level1, Level2, Multi level)
IGP can allocate Segment ID as MPLS Label
  No other signalling protocol required
  BGP can also be used in certain case
Push traffic into the tunnel
  Manual, Auto-route
  Tunnel fallback provides less traffic disruption

## Slide 5: SR IGP Control Plane
IS-IS for SR
  Uses TLV and Sub-TLV to play with Prefix and Adj SID
  Requires wide metric support to be enabled
  Enables MPLS on all non-passive interfaces
    Even if no neighbors are there
  IS-IS starts with dealing with SRGB, Prefix SID and Adj SID
  Forwarding tables are programmed
router isis 1
address-family ipv4 unicast
metric-style wide
segment-routing mpls
interface loopback 0
prefix-sid index 1
Enables SR Control Plane and MPLS Data Plane

## Slide 6: SR IGP Control Plane
OSPFv2 for SR
  Uses (extended) Opaque LSA
    Opaque Type 4 (to carry SR capabilities)
    Opaque Type 7 (for Prefix SID)
    Opaque Type 8 (for Adj-SID)
    Opaque LSA adds different sub-TLV
    Some Old Opaque LSAs:
      Type 9: Link-local scope
      Type 10: Area-local scope (Used by TE)
      Type 11: AS-wide scope
router ospf 1
segment-routing mpls
area 0
interface loopback 0
prefix-sid index 1
Enables SR Control Plane and MPLS Data Plane

## Slide 7: MPLS TE
Each router start to advertise SIDs

## Slide 8: Lab - Demo of SR Control Plane
Segment Routing Control Plane

## Slide 9: Thank you !!