## Slide 1: OSPF Routing Protocol
Note
M Abdullah Al Naser
Datacom Professional
mnaser.net@gmail.com
Version 0.1

## Slide 2
A big disclaimer:

## Slide 3: OSPF Routing Protocol
Note

## Slide 4: OSPF Characteristics
Link-state Routing Protocol
  Link: Interface of the router
  State: Description of the interface
  Can see full topology within area
Uses Dijktra’s Shortest Path First (SPF) algorithm
Classless
  Supports VLSM
Efficient / Scalable / Secure / Fast convergence
Supports Multi Area
IP Protocol number 89

## Slide 5: Link State Routing Process
Router learns own directly connected networks
Discovers neighbor
Builds LSA
Floods LSA and stores incoming LSAs in LSDB
Runs SPF to build loop-free SPT

## Slide 6: Basic Configuration
Network statement
  Enable interfaces in OSPF process that falls within the range
  Sends Hello via OSPF enabled interfaces
  Advertises networks that falls within the range
  # conf t
  router ospf 1
  network 192.168.1.0 0.0.0.255 area 0

## Slide 7: Basic Configuration
Interface Specific Configuration
  Enable interface in OSPF process
  Sends Hello via that interface
  Advertises network
  # conf t
  interface gi0/0
  ip ospf 1 area 0
# show ip ospf neighbor
# show ip protocols

## Slide 8: What’s inside a Hello
Router ID **
Hello interval and Dead interval *
Active neighbors (if any)
Area ID *
IP addresses of DR and BDR (for broadcast link)
Subnet Mask *
Authentication parameters *
Interface Priority
Stub Area Flags *

## Slide 9: OSPF States
Down
  No Hello detected
Attempt
  For NBMA (static neighbor)
Init
  Router receives a Hello
2-Way
  Router sees itself as a neighbor in a received Hello
DR/BDR Election (for broadcast link)

## Slide 10: OSPF States
Exstart
  Master/Slave election
  Router having highest numerical RID will be the master
Exchange
  Master sends the DBD first; then by Slave
  DBD contains summary of the LSDB
  IP MTU of interfaces should be identical (overridable)

## Slide 11: OSPF States
Loading
  Send LSAck for DBD
  Compare information on DBD with LSDB
  Send LSR for additional info
  LSU is in response of LSR
  LSU contains LSAs
Full
  Sends LSAck for LSR
  LSBDs are synched

## Slide 12: DR/BDR Election
DR is essential in multi-access (broadcast) links
Eliminates the need of full-mesh adjacency
  n(n-1)/2
Reduces LSA flooding impact
Requires a BDR for fail-over

## Slide 13: DR/BDR Election
Election criteria
  Highest interface priority
  Highest RID
Priority ranges from 0 to 255
  255 for DR (Hub router)
  254 for BDR (Hub router)
  0 for DROther (Spoke routers)
    Doesn’t contest in election
  1 is set by default
First router will wait 40s to declare itself as DR
  Wait timer is 40s (by default)

## Slide 14: DR/BDR Election
States:
  DR to BDR: Full
  DROther to DR: Full
  DROther to BDR: Full
  DROther to DROther: 2-Way
DR and BDR receive LSAs from all DROthers
  Only DR floods LSAs to all DROther
DR/BDR is for per multi-access link; not per area
When DR returns it can’t take over the role
  Non preemptive

## Slide 15: DR/BDR Election
Interface type P2P avoids DR/BDR election
  Eliminates Type 2 LSA flooding
  Keeps LSDB smaller
In case of interface type mismatch:
  Routers will form adjacency
  Routers will exchange LSAs
  But routers will exclude the link from SPF calculation

## Slide 16: Network Link Types
Transit
  A link that carries neighborship or adjacency (on broadcast links)
  Represented by the IP of DR
Point-to-Point
  A link that carries adjacency (on P2P links)
  P2P type creates two links:
    1. A link that identifies neighbor RID for that segment
    2. A stub network with subnet mask to advertise that network
  Represented by neighbor’s RID

## Slide 17: Network Link Types
Stub
  A link that doesn’t carry any neighborship or adjacency
  Usually, a LAN facing interface
  A “secondary” network is always a stub network and never forms neighborship
  Represented by IP network
Virtual Link
  Represented by neighbor’s RID

## Slide 18: OSPF Packet Types
Hello
  For neighbor discovery
DBD
  Contains summary of LSDB
LSR
  To request for additional info
LSU
  Contains LSAs
LSAck
  OSPF uses RTP for reliability

## Slide 19: Multicast in OSPF
All OSPF router send Hello using:
  IP: 224.0.0.5
  MAC: 01:00:5e:00:00:05
All DROther send LSA using:
  IP: 224.0.0.6
  MAC: 01:00:5e:00:00:05

## Slide 20: Administrative Distance
Defines the preference of OSPF over other protocols
Default AD value is 110
Must be identical on all routers
  To avoid loops or sub-optimal routing
A golden Rule: Longest Prefix Match > AD > Metric

## Slide 21: OSPF Router ID
Router ID is the identifier of an OSPF router
  Must be unique in an area
  Should be unique network wide
A 32-bit integer value
  Looks like an IPv4 address; but not an IPv4 address actually
Selection criteria:
  Configured manually (should be a best practice)
  Highest IPv4 address of loopback interface
  Highest IPv4 address of physical interface

## Slide 22: OSPF Timers
Hello timer
  10s for broadcast and p2p interfaces (by default)
Dead timer
  40s; 4 times of Hello (by default)
# conf t
int face gi0/0
ip ospf hello-interval 3 //also sets Dead to 12s (4 times) automatically
ip ospf dead-interval 12
ip ospf dead-interval minimal hello-multiplier 3
//sets Dead to 1s; and Hello to 333ms (1/3 of Dead)
Hello and Dead intervals must be identical at both end
BFD can be deployed for quicker link failure detection

## Slide 23: OSPF Timers
Wait timer
  A time to wait for first router to declare itself as DR
Retransmit timer

## Slide 24: OSPF Metric
Cost is the metric in OSPF
Cost = Reference BW / Interface BW
  Ref BW = 100 Mb (by default)
For Fast Ethernet link:
  Cost = 100 Mb / 100 Mb = 1
For Gigabit Ethernet link:
  Cost = 100 Mb / 1000 Mb = 1
    Fractional value isn’t supported

## Slide 25: OSPF Metric
# conf t
router ospf 1
auto-cost reference-bandwidth 1000
interface gi0/0
bandwidth 64 //in Kbps
  Cost = 100000000 / 64000 = 1562
Reference BW should be identical on all routers
  To avoid sub optimal routing
Cost can be configured straight forward
# conf t
interface gi0/0
ip ospf cost 10

## Slide 26: OSPF Maximum Path
OSPF supports multiple equal cost path (if any)
  4 equal cost path (by default in Cisco)
  Can be configured up to 32 path (depending on platform)
# conf t
router ospf 1
maximum-path 6

## Slide 27: Shutting Down OSPF
In case of:
  Troubleshooting
  Network migration
# conf t
router ospf 1
shutdown

## Slide 28: Passive Interface
Restricts Hello to be sent via an interface
All the LAN facing interfaces should be passive
Secure network preventing unwanted neighbors and routes
Saves network bandwidth and processing
# conf t
router ospf 1
passive-interface default
no passive-interface gi0/0

## Slide 29: Authentication
To prevent any unwanted neighborship
OSPF supports:
  Plain Text
  MD5
  HMAC-SHA (from IOS 15.4(1)T)

## Slide 30: Authentication
Plain Text
# conf t
interface gi0/0
ip ospf authentication-key OSPF1234
ip ospf authentication //for interface level
router ospf 1
area 0 authentication //for area level
  Key string must be identical

## Slide 31: Authentication
MD5
# conf t
interface gi0/0
ip ospf message-digest-key 1 md5 OSPF1234
ip ospf authentication message-digest //for interface level
router ospf 1
area 0 authentication message-digest //for area level
  Key number and key string must be identical

## Slide 32: Authentication
HMAC-SHA
# conf t
key-chain MYCHAIN
key 1
cryptographic-algorithm hmac-sha-512
key-string OSPF1234
interface gi0/0
ip ospf authentication key-chain MYCHAIN //for interface level
  Key number and key string must be identical

## Slide 33: Authentication
# debug ip ospf packet
  Auth 0: No authentication
  Auth 1: Plain text authentication
  Auth 2: MD5 Authentication

## Slide 34: TTL Security Check
Protects OSPF control plain from remote attack
When enabled:
  Router will send OSPF packet with TTL 255
  Router will receive OSPF packet only if TTL is 255 in received packet
Only packets from directly connected router will be accepted
Default TTL value for OSPF packet is 1
# conf t
router ospf 1
ttl-security all-interfaces

## Slide 35: TTL Security Check
# conf t
router ospf 1
ttl-security all-interfaces //accepts packet with TTL 255
ttl-security all-interfaces //accepts packet with TTL from 155 to 255
interface gi0/0
ip ospf ttl-security
Not applied to virtual links or sham links (by default)
# area virtual-link ttl-security
# area sham-link ttl-security

## Slide 36: Route Redistribution
Different protocols don’t share routing information with each other
Redistribution between protocols is required
  Connected and static routes can also be redistributed
Redistribution happens outbound
Redistribution should be mutual
Should be configured carefully
  To prevent routing table flapping or loop

## Slide 37: Route Redistribution
Different protocol’s metric are not compatible with each other
  RIP: Hop count
  EIGRP: K Value
  OSPF/IS-IS: Cost
  BGP: Multiple attributes
Seed metric is required to be configured
For multipoint redistribution route tagging to be configure
  To prevent routing loop
  Protocol A  Protocol B X Protocol A
  Set tag 1234 Match tag 1234 (deny)

## Slide 38: Route Redistribution in OSPF
OSPF has two types of External route
  External Type 1
  External Type 2 (by default)
Seed metric (by default):
  From BGP: 1
  From other protocols: 20
For External Type 2:
  Cost is always 20 (except from BGP)
  Forward metric to ASBR works in background
For External Type 1:
  Cost = 20 + Forward metric

## Slide 39: Route Redistribution in OSPF
# conf t
router ospf 1
redistribute static subnets metric-type 1 metric 5
/
redistribute connected subnets
/
redistribute bgp 100 subnets route-map RM-MAP
/
default-information originate always
External routes are redistributed using Type 5 LSA
ASBR’s RID is propagated by ABR using Type 4 LSA

## Slide 40: Route Redistribution in OSPF
Selection of External routes
  Lowest Seed Metric sent by ASBR
  Lowest path cost towards ASBR (Forwarding Metric)
  Highest RID of ASBR
Redistributing BGP into OSPF results in loss of BGP attributes
Shouldn’t redistribute full internet routing table from BGP

## Slide 41: Multi Area OSPF
Key Terms
Backbone Area
Non-backbone Area
Backbone Router
Non-backbone Router
Area Border Router (ABR)
Autonomous System Border Router (ASBR)
  At least one interface should be Area 0; Loopback also works

## Slide 42: Multi Area OSPF
Helps to reduce the size of LSDB
Less SPF calculation inside an area
  SFP is performed independently for each area
Router in an area has no visibility of other area
  Between areas no topology information is shared
Reduces the LSA update size to keep under interface MTU
  Fragmentation causes a big problem
Number of ABR is an area should be limited
  ABR keeps LSDB of multiple area (including Area 0)

## Slide 43: Multi Area OSPF
All areas need to connect to Backbone Area
  Area 0.0.0.0, has the transit capability
  Prevents Loop
  Virtual Links for exceptional case
Two levels of hierarchy:
  Backbone Area
  Non-Backbone Area

## Slide 44: LSA
Link State Advertisement
  Not a packet but a data structure
  A piece of puzzle of the LSBD
  Travels inside a LSU
A LSA may contain multiple link information
  Maintains Sequence Number
    A 32-bit number for version controlling
LSA is periodically advertised in every 30 min (by default)
  To keep the LSDB synchronized and identical
  Adds random delay (based on when the LSA was created) to prevent big event

## Slide 45: LSA
Receiving router floods LSA is updated info inside
In OSPF there are 11 LSAs
  Whereas in IS-IS there are only 2 Levels
Why lot of LSAs in OSPF?
  Answer: Critical design requirements and Scalability (not Simplicity)

## Slide 46: LSDB
The core of OSPF protocol
LSDB fields are:
  Link ID: Identifies the object
  Adv Router: Router ID of LSA originator
  AGE: Age of the LSA on which router the command is executed
  Seq#: The sequence number to protect out-of-order LSA
  Checksum: To verify integrity of LSA during flooding
  Link Count: Number of links of router in Type 1 LSA
Flooding LSAs and building LSBDs are not enough for routing table
Routing and Forwarding table require an additional SFP calculation

## Slide 47: OSPF LSA Types
Type 1: Router LSA
  Router generates a single LSA containing multiple link
  Floods within the area
Type 2: Network LSA
  Handles DR/BDR stuffs in broadcast links
  Can be omitted in P2P links
    DR/BDR election can prolong convergence time
  Floods within area

## Slide 48: OSPF LSA Types
Type 3: Summary Net Link LSA
  Contains multi area information
  ABR re-originates LSA; acts as the Adv Router
    ABR converts Type1 to Type 3
  Not summarized by default
    Propagates other areas link failure
    Need to manually summarized by the ABR
    IP addressing plan should be contiguous
  Adds Null0 summary route to prevent forwarding loop

## Slide 49: OSPF LSA Types
Type 4: ASBR Summary LSA
  ABR of originating area propagates ASBR’s RID to other areas
Type 5: External LSA
  Contains external routes outside of OSPF domain
    Redistributed from other protocols, connected, static, default-origination
  Generated by ASBR
  Floods throughout entire OSPF domain except STUB areas
  Routes can be summarized by ASBR
  Adds Null0 summary route

## Slide 50: OSPF LSA Types
Type 7: NSSA LSA
  Contains external routes outside of OSPF domain
    Type 5 is not permitted in STUB areas
  Generated by ASBR in NSSA area
  Floods within NSSA area
  ABR in NSSA area converts it from Type 7 to Type 5
    No Type 4 LSA for ASBR’s information

## Slide 51: Special Areas
Keeps LSA flooding minimum; Keeps LSDB smaller
Less SPF calculation; Smaller Routing table
Provides fault isolation
  Can be useful for critical enterprise network design
  Not suitable for service provider networks
Types:
  Stub Area
  Totally Stub Area (T. Stub)
  Not So Stubby Area (NSSA)
  Totally Not So Stubby Area (T.NSSA)

## Slide 52: Stub Area
“IA” route sent by ABR
Additional default route sent by ABR (as Type 3)
No “External” route via backbone area
  No Type 4 LSA
  No Type 5 LSA
No ASBR is allowed

## Slide 53: T.Stub Area
No “IA” route sent by ABR
Only default route sent by ABR (as Type 3)
No “External” route via backbone area
  No Type 4 LSA
  No Type 5 LSA
No ASBR is allowed

## Slide 54: NSSA
“IA” route sent by ABR
Additional default route sent by ABR (as Type 3)
No “External” route
  No Type 4 LSA
  No Type 5 LSA
ASBR is allowed
  Introduces Type 7 LSA
  Floods within NSSA area
  Propagated by ABR to other areas as Type 5 (But No Type 4 for ASBR info)

## Slide 55: T.NSSA
No “IA” route sent by ABR
Only default route sent by ABR (as N2 by default)
No “External” route
  No Type 4 LSA
  No Type 5 LSA
ASBR is allowed
  Introduces Type 7 LSA
  Floods within NSSA area
  Propagated by ABR to other areas as Type 5 (But No Type 4 for ASBR info)

## Slide 56: NSSA P bit
a

## Slide 57: OSPF LSA Types
LSA Flooding Scope
  * Indicates the "Default Route"
LSA | Normal | Stub | T.Stub | NSSA | T.NSSA
1 | Y | Y | Y | Y | Y
2 | Y | Y | Y | Y | Y
3 | Y | Y * | N * | Y * | N *
4 | Y | N | N | N | N
5 | Y | N | N | N | N
7 | N | N | N | Y | Y

## Slide 58: Virtual Link
A way to connect an isolated area to the backbone area
Adds complexity and should not be a good practice
Need to configure between ABR 1 (that connects Area0) and ABR 2 connecting isolated area
  Uses RID of ABR1 and ABR2; not their IP addresses
ABR2 stores full LSDB of Area 0
  ABR2 send Type 3 routes to downstream routers
  ABR2 may summarize the Type 3 routes
DNA = Do not Advertise

## Slide 59: OSPF Route Types
Intra Area “O”
Inter Area “O IA”
External
  Type 1 “E1”
  Type 2 “E2”
NSSA External
  Type 1 “N1”
  Type 2 “N2”

## Slide 60: OSPF Path Selection Process
O > O IA > N1 > E1 > N2 > E2 (from IOS 15.1(2)S; RFC 3101)
  1. Intra Area Route “O”
  2. Inter Area Route “O IA”
  3. NSSA Type 1 Route “N1”
  4. External Type 1 Route “E1”
  5. NSSA Type 2 Route “N2”
  6. External Type 2 Route “E2”
O > O IA > E1 > N1 > E2 > N2 (on older IOS; RFC1587)

## Slide 61: Route Summarization
Summarization must be done on ASBRs and ABRs
  Summary route needs at least one contributing route
  The cost of the summary route is derived from the lowest cost of a contributing route
  Summarization should be done to all neighbors
Advantages:
  Saves CPU, Memory and BW
  Hides smaller prefixes
  Helps to keep routing stable
  Helps to run SPF faster
Disadvantages:
  Forwards traffic to unused network
  Improper configuration may cause suboptimal routing
  Destroys MPLS LSP

## Slide 62: Route Filtering
Filtering must be done on ASBRs and ABRs
  ASBR can filter Type 5 LSA
  ABR can filter Type 3 LSA
Shouldn’t be configured to filter Type 1 LSA
  OSPF can’t filter Type 1 LSA
  Local filtering can be configured on any edge node of an area
  Shouldn’t be configured on any intermediary node of an area
  Causes traffic blackholing

## Slide 63: SPF Calculation
Finding SPT from root
  R1 for example
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4
TENT | 
PATH | 

## Slide 64: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
PATH | 
R1-R1 | 0
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 65: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
PATH | 
R1-R1 | 0
R1-R2 | 2
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 66: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
PATH | 
R1-R1 | 0
R1-R2 | 2
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 67: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 68: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
R3-R1 | 4
R3-R2 | 1
R3-R5 | 3
R3-R6 | 4
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 69: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
R3-R1 | 4
R3-R2 | 1
R3-R5 | 3
R3-R6 | 4
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R3-R5 | 3
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 70: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
R3-R1 | 4
R3-R2 | 1
R3-R5 | 3
R3-R6 | 4
R4-R2 | 2
R4-R5 | 2
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R3-R5 | 3
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 71: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
R3-R1 | 4
R3-R2 | 1
R3-R5 | 3
R3-R6 | 4
R4-R2 | 2
R4-R5 | 2
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R3-R5 | 3
R3-R6 | 4
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 72: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
R3-R1 | 4
R3-R2 | 1
R3-R5 | 3
R3-R6 | 4
R4-R2 | 2
R4-R5 | 2
R5-R3 | 4
R5-R4 | 6
R5-R6 | 2
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R3-R5 | 3
R3-R6 | 4
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 73: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
R3-R1 | 4
R3-R2 | 1
R3-R5 | 3
R3-R6 | 4
R4-R2 | 2
R4-R5 | 2
R5-R3 | 4
R5-R4 | 6
R5-R6 | 2
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R3-R5 | 3
R3-R6 | 4
R2-R4 | 5
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 74: SPF Calculation
Finding SPT from root
  R1 for example
TENT | 
R1-R2 | 2
R1-R3 | 2
R2-R1 | 1
R2-R3 | 4
R2-R4 | 5
R3-R1 | 4
R3-R2 | 1
R3-R5 | 3
R3-R6 | 4
R4-R2 | 2
R4-R5 | 2
R5-R3 | 4
R5-R4 | 6
R5-R6 | 2
R6-R3 | 4
R6-R5 | 5
PATH | 
R1-R1 | 0
R1-R2 | 2
R1-R3 | 2
R3-R5 | 3
R3-R6 | 4
R2-R4 | 5
R1
R2
R3
R4
R5
R6
2
2
1
4
4
1
3
2
1
4
2
3
2
2
5
4

## Slide 75: Prefix Suppression
P2P links aren’t useful for traffic delivery
  Loopbacks can be used for iBGP
Excludes “STUB Links” in SPF calculation
  P2P means the Transit links
  Suppresses “STUB Links of P2P links only” from Type 1 LSA
Reduces LSDB size
  Helps to run SPF faster
Keeps routing table stable
  Less SPF run
  Smaller routing table

## Slide 76: OSPF Convergence
Link/Node failure causes:
  Failure detection  BFD
  Failure propagation  Reduced LSA throttling timer
  Processing new information  SPF Calculation
  Updating RT and FT  depends on HW capacity; can not be tuned
Convergence is control plane event
Convergence is reactive

## Slide 77: OSPF Fast Re-route
FRR (or Protection) is a data plane event
Protection is a hot-standby as soon as failure is detected
Post convergence path can be calculated before failure occurs
  Path must be loop free; but always can not be achieved with LFA, rLFA
  LFA and rLFA require LDP signaling even in non MPLS network
  TI-LFA in SR is the latest solution; 50ms
FRR is proactive (whereas convergence is reactive)

## Slide 78: Microloop in OSPF
Microloop is a long-lasting problem in IGP
Microloop may happen in FRR
May cause traffic drop during convergence time
SR can solve the problem using TI-LFA

## Slide 79: OSPF Multi Area Adjacency
A feature to form multiple adjacency over a single link
  One adjacency for Area 0
  Another adjacency for Area n
Useful to prevent sub-optimal traffic forwarding between areas

## Slide 80: OSPF Stub Router
A

## Slide 81: Deployment Consideration
For Service Provider
Suitable for deploying RSVP TE and SR
  Capabilities have been extended
Can be used in IP core
  Multi domain IGP is a good choice for Seamless/Unified MPLS
Can be used as PE-CE protocol in L3VPN
  Should never be used to push route in global table
If not necessary don’t use multi area OSPF
  To keep design simple; multi domain OSPF is a good option
  RSVP-TE is very hard to deploy

## Slide 82: Deployment Consideration
For Enterprise
Suitable for deploying in typical 3-tier design
  Between Core and Aggregation
  Host gateways are in Aggregation nodes
Multi area is a good consideration for large network
Can be run over tunnels
  To connect multiple location over ISP network
  GRE, mGRE, DMVPN, etc

## Slide 83: Deployment Consideration
For Data Center
DC now a days uses Spine and Leaf topology
OSPF can be used as underlying protocol for VXLAN VTEPs
  But IS-IS seems more popular for this
Multiple DC location meshed can cause more LSA flooding
  eBGP is getting popularity day by day

## Slide 84: Thank you!