## Slide 1: Segment Routing with MPLS Data Plane (SR-MPLS 101)

## Slide 2
The objective of this presentation is to discuss the need and benefits of Segment Routing with MPLS data plane (SR-MPLS) along with some shortcomings of LDP/RSVP-TE based MPLS in production network.
This presentation maybe useful for a network engineer running typical MPLS network for years to learn “Segment Routing” from very basic and also for a CxO to think about to move towards SDN era for the sake of service quality.

## Slide 3: IP and Routing
A method to forward packets
  Based on destination IP address
  Same lookup process at each hop takes time
Replaced Frame Relay, ATM in telecommunication network
  IP came as a best effort forwarding capability
  Variable length packet header
  Connectionless; reliability ensured by transport layer
  Flexible but has less QoS capability
TE not possible

## Slide 4: MPLS Intro
A label based approach to forward traffic
  Labels are in a fixed 32-bit header
  Label Distribution Protocol (LDP)
  Label Operation: PUSH, SWAP, POP
Overlay tunnelling for customer services
  L3VPN, L2VPN
  BGP-free core; RR requires for large network
TE possible: RSVP-TE

## Slide 5: MPLS LDP
MP-BGP
R1
R2
R3
R4
CE1
CE2
Control Plane
Label distribution from R4 to R1
LDP
LDP
LDP
Local Label
404
Local Label
304
Out Label
404
Local Label
204
Out Label
304
Local Label
104
Out Label
204
Local Label
1004
Out Label
4004
Local Label
4004

## Slide 6: MPLS LDP
MP-BGP
R1
R2
R3
R4
CE1
CE2
Forwarding Plane
Traffic forwarding from R1 to R4
IP
4004
204
LDP
LDP
LDP
IP
4004
304
IP
4004
IP
IP
PHP
BGP Free Core
(RR may require in production)
IP
Label pushed
Label unchanged
Label swapped
Label popped

## Slide 7: MPLS TE
To steer traffic through longer path
  To utilize unused links
  To avoid congestion on busy links
RSVP-TE
  Creates circuits; state is signalled hop-by-hop
  Need to configure link constraints (BW and other attributes)
  Distribute TE info using IGP extension
  PCALC (CSPF) to calculate best path
  Carries TE labels to signal tunnel from head-end to tail-end PE
Push traffic into the tunnel
  Manual, Auto-route
  Tunnel fallback provides less traffic disruption

## Slide 8: MPLS TE
Shortest Path
R1
R2
R3
R4
CE1
CE2
Control Plane
RSVP PATH messages reserve BW and request for MPLS label
R5
PATH
PATH
PATH
PATH
Head-end
Tail-end

## Slide 9: MPLS TE
Shortest Path
R1
R2
R3
R4
CE1
CE2
Control Plane
RSVP RESV messages carry MPLS label
RESV
RESV
RESV
TE
Path
RESV
TE PATH is signaled “hop-by-hop” based on ERO !!!
R5
PATH
PATH
PATH
PATH
Head-end
Tail-end

## Slide 10: MPLS TE
Shortcomings:
Tunnel is not bidirectional
IGP tracks link constraints and floods periodically
  Maintains state
  TE tunnel need to be re-optimized frequently
RSVP-TE isn’t ECMP friendly (N2*K tunnel required)
  Doesn’t scale well with inter-domain (IGP) network
Additional overhead for
both router and it’s administrator
Why is RSVP-TE still useful?

## Slide 11: Fast Reroute (FRR)
Widely used in carrier backbone
  Pre-computed backup path
  Backup next-hop installed in forwarding table
  Minimize reconvergence time
  Can be used to protect tunnels (links/nodes)
Must have LFA – Loop Free Alternative
Doesn’t provide optimum path all the time
Very difficult to configure and manage

## Slide 12: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with Loop Free Alternative (LFA) - RFC 6571
R5
1
1
1
5
n
IGP COST
Primary Next-hop
Backup Next-hop
1
R6
1
CE1
CE2

## Slide 13: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with Loop Free Alternative (LFA)
R5
1
1
1
5
Primary Next-hop
1
R6
1
Can’t be a
Backup Next-hop
R1 itself is
R5’s next-hop
n
IGP COST
Micro-loop happens !!!
CE1
CE2

## Slide 14: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with Remote Loop Free Alternative (rLFA) – RFC 7490
R5
1
1
1
5
Primary Next-hop
1
R6
1
Can’t be a
Backup Next-hop
R1 itself is
R5’s next-hop
R6 can be R1’s backup next-hop
Requires LDP tunnelling for rLFA
n
IGP COST
CE1
CE2

## Slide 15: Fast Re-route (FRR)
R1
R2
R3
R4
FRR with rLFA is not always Loop Free
R5
1
1
1
5
Primary Next-hop
1
R6
9
Can’t be a
Backup Next-hop
R1 itself is
R5’s next-hop
R6 can’t be R1’s backup next-hop
Because R1 itself is in R5’s transit path
n
IGP COST
We need next-gen TI-LFA
with micro-loop avoidance capability
and 100% coverage
CE1
CE2

## Slide 16: IGP-LDP Sync
Primary Path
R1
R2
R3
R4
CE1
CE2
Primary Path Goes Down (!)
Customer traffic re-routed via alternative path
R5
LDP
LDP
LDP
LDP
Alternative
Path
My next-hop towards R4 is R5

## Slide 17: IGP-LDP Sync
Primary Path
R1
R2
R3
R4
CE1
CE2
Primary Path Goes Up (!!!)
Customer traffic dropped when re-routed via primary path – BROKEN LSP
LDP
LDP
LDP
LDP
Alternative
Path
IGP
LDP On the Way
My next-hop towards R4
is R3
IGP-LDP Sync requires to be configured on each LDP enabled link
R5

## Slide 18: MPLS-TE with FRR
Link Protection
Primary Path
R1
R2
R3
R4
CE1
CE2
Primary
Tunnel
R6
Backup Tunnel
R5
PLR
MP

## Slide 19: MPLS-TE with FRR
Node Protection
Primary Path
R1
R2
R4
CE1
CE2
Primary
Tunnel a
R5
R6
Backup Tunnel
R3
PLR
MP

## Slide 20: MPLS-TE with FRR
SRLG Protection
Primary Path
R1
R2
R4
CE1
CE2
Primary
Tunnel a
R5
R6
Backup Tunnel
R3
PLR
MP

## Slide 21: MPLS-TE with FRR
Typical FRR may provide sub-optimal path
R1
R2
R3
CE1
CE3
R4
R5
R6
CE2
5
n
IGP COST
1
1
5
5
5
1
● Based on circuit concepts
● Sub-optimal Path
● Not ECMP friendly
● Causes link congestion
Primary Path
Expected Backup Path
Actual Backup Path
Link Protection
Configured

## Slide 22: MPLS (Cont.)
Shortcomings:
Doesn’t deal with performance anymore
  CEF, ASIC etc
Requires IGP-LDP synchronization
TE is not scalable
FRR is supported but very difficult to configure and manage
Not suitable for very large carrier network

## Slide 23
SR-MPLS
Segment Routing with MPLS data plane

## Slide 24: SR-MPLS
LDP+RSVP control plane is complex
SR control plane with IGP
  SR is an extension of IGP
  MPLS is still as the forwarding plane
No LDP, No RSVP-TE are required

## Slide 25: SR-MPLS
R1
R2
R3
R4
CE1
R5
R6
R9
R8
R7
CE2
IP
VPN
16009
IP
VPN
16009
IP
IP
VPN
16009
IP
VPN
16009
IP
VPN
16009
IP
VPN
16009
IP
VPN
PHP
IP
VPN
16009
IP
One of the major ideas behind SR is to keep “Transport Label” consistent “per segment”
PUSH
CONTINUE
POP
CE1
CE2

## Slide 26: SR-MPLS
R1
R2
R3
R4
CE1
R5
R6
R9
R8
R7
CE2
IP
VPN
16009
IP
PHP
Traffic is forwarded “Segment by Segment”
16006
16004
IP
VPN
16009
16006
16004
IP
VPN
16009
16006
IP
VPN
16009
16006
IP
VPN
16009
PHP
IP
VPN
16009
IP
VPN
IP
VPN
16009
PHP
IP
“Ordered list of segment” is encapsulated by source node
PUSH
CONTINUE
POP

## Slide 27: SR-MPLS
Primary Path
Backup Path
First Segment
Second Segment

## Slide 28: SR-MPLS
Source routing paradigm – SPRING
  SPRING – Source Packet Routing in Networking
  Source node can encapsulate path information using label stack
  Intermediate nodes don’t need to maintain any state
Inserts an “ordered list of segment” with the packet
  A segment is an instruction – topological, service chaining etc
  Segment ID (SID) is equivalent to the LDP Label (in case of SR-MPLS)
  Each SID indicates a segment; the top SID indicates active segment
IGP carries SID information
  No LDP, No RSVP

## Slide 29: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Control Plane
Label generation on each router to reach R4
IGP
IGP
IGP
Index Value: 4
Local Label
16004
Out Label
16004
Local Label
16004
Out Label
16004
Local Label
16004
Out Label
16004
Local Label
1004
Out Label
4004
Local Label
4004
SRGB (all router)
16000 - 23999
In Label = SRGB Base + Originator Node’s SID Index
Out Label = Next-hop’s SRGB Base + Originator Node’s SID Index
Transport (Out) labels are consistent

## Slide 30: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Forwarding Plane
Traffic forwarding from R1 to R4
IP
4004
16004
IGP
IGP
IGP
IP
4004
16004
IP
4004
IP
IP
PHP
BGP Free Core
(RR may require in production)
IP
Transport (Out) labels are consistent
TE and FRR would be easier

## Slide 31: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Control Plane
Label generation on each router to reach R4
IGP
IGP
IGP
Index Value: 4
Local Label
18004
Out Label
19004
Local Label
17004
Out Label
18004
Local Label
16004
Out Label
17004
Local Label
1004
Out Label
4004
Local Label
4004
What if the SRGB is not same on routers
R1: 16000 - 16999
R2: 17000 - 17999
R3: 18000 - 18999
R4: 19000 - 19999
In Label = SRGB Base + Originator Node’s SID Index
Out Label = Next-hop’s SRGB Base + Originator Node’s SID Index
Transport (Out) labels are inconsistent

## Slide 32: SR-MPLS
MP-BGP
R1
R2
R3
R4
CE1
CE2
Forwarding Plane
Traffic forwarding from R1 to R4
IP
4004
17004
IGP
IGP
IGP
IP
4004
18004
IP
4004
IP
IP
PHP
BGP Free Core
(RR may require in production)
IP
Transport (Out) labels are inconsistent
TE and FRR would be difficult

## Slide 33: SR-MPLS
Global Segment
Global segments are for routers’ loopback
Assigned from Segment Routing Global Block (SRGB)
  Ranges from 16000 to 23999 for interoperability
  Intended design; highly recommended to keep it same on all router
Keeps transport label consistent per segment (i.e. within IGP domain)
Local Segment
Local segments are for routers’ P2P links
  Assigned from dynamic label range
Supports advanced traffic engineering and FRR
  TE path doesn’t need to be signalled hop-by-hop

## Slide 34: Segment ID
IGP Segment
Prefix Segment
Node Segment
Anycast Segment
Adjacency Segment
BGP Segment
Prefix Segment
EPE Segment
Peer Node Segment
Peer Adj Segment
Peer Set Segment
IGP Control Plane
BGP Control Plane

## Slide 35: Segment ID
Prefix SID: for routers’ loopbacks
  Assigned from SRGB
Adjacency SID: for routers’ P2P links
  Assigned from dynamic range
R1
R4
R2
R3
Prefix SID
R1: 16001
Adjacency SID
R1-R2: 24012
Prefix SID
R2: 16003
Adjacency SID
R3-R2: 24032
R3-R4: 24034
Prefix SID
R4: 16004
Adjacency SID
R4-R2: 24042
R4-R3: 24043
Prefix SID
R2: 16002
Adjacency SID
R2-R1: 24021
R2-R3: 24023
R2-R4: 24024

## Slide 36: SID List
Explicit path can be defined using local segments
Useful for TE and FRR
R1
R4
R2
R3
IP
VPN
16004
24023
16002
CE1
CE2
“Ordered list of segment” is encapsulated by source node
First: Go to R2
Second: go through R2’s Gi0/1
Third: go to R4
Gi0/1
Gi0/2
1
n
IGP COST
1
5
1

## Slide 37: SR-MPLS Features
FRR with TI-LFA
  Avoids micro-looping
Scalable TE
  SR Policy; and no more tunnel
Can be a part of SDN (for inter-domain network)
  PCEP and BGP-LS

## Slide 38: FRR with TI-LFA
Fast Reroute with TI-LFA
Topology Independent LFA
  Sub 50ms convergence time
  Minimizes amount of dropped traffic during convergence
Protects links, nodes and SRLGs
Maintains better SLA

## Slide 39: FRR with TI-LFA
R2
TI-LFA Link Protection
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Topology is fully functional
R1’s Primary path is in forwarding table
1
IP
VPN
16003
“Ordered list of segment” for primary path
10
1

## Slide 40: FRR with TI-LFA
TI-LFA Link Protection
R1 is aware of the backup path in advance in case of link failure to R2
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
1
10
PLR
Protected Link
1

## Slide 41: FRR with TI-LFA
TI-LFA Link Protection
R1 prunes protected link before link failure occurs and find out post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
Protected Link
1

## Slide 42: FRR with TI-LFA
TI-LFA Link Protection
R1 defines the P Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
P Node is such node which can reach source (R1) without using protected link
10
1
P
PLR
Protected Link
1

## Slide 43: FRR with TI-LFA
TI-LFA Link Protection
R1 defines the Q Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Q Node is such node which can reach destination (R3) without using protected link
10
1
Q
PLR
Protected Link
1
P

## Slide 44: FRR with TI-LFA
TI-LFA Link Protection
P Space and Q Space
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
Protected Link
1
Q
P

## Slide 45: FRR with TI-LFA
TI-LFA Link Protection
R1 builds SID-list based on each segment it found along the post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
IP
VPN
16003
24045
16004
Protected Link
“Ordered list of segment” for post convergence path
1
Q
P
Q
P

## Slide 46: FRR with TI-LFA
TI-LFA Link Protection
R1 programs the precomputed SID-List it in forwarding table
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
Protected Link
PLR
IP
VPN
16003
24045
16004
IP
VPN
16003
“Ordered list of segment” for primary path
“Ordered list of segment” for post convergence path
1
Q
P

## Slide 47: FRR with TI-LFA
TI-LFA Link Protection
When protected link goes down R1 instantly use post convergence SID-list even before IGP converges new path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
Protected Link
PLR
Q
P
IP
VPN
16003
24045
16004
“Ordered list of segment” for post convergence path
1

## Slide 48: FRR with TI-LFA
R2
TI-LFA Node Protection
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Topology is fully functional
R1’s Primary path is in forwarding table
1
IP
VPN
16003
“Ordered list of segment” for primary path
10
1

## Slide 49: FRR with TI-LFA
TI-LFA Node Protection
R1 is aware of the backup Node in advance in case of failure of R2
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
1
10
PLR
Protected Node
1

## Slide 50: FRR with TI-LFA
TI-LFA Node Protection
R1 prunes protected node before node failure occurs and find out post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
1
Protected Node

## Slide 51: FRR with TI-LFA
TI-LFA Node Protection
R1 defines the P Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
P Node is such node which can reach source (R1) without using protected node
10
1
P
PLR
1
Protected Node

## Slide 52: FRR with TI-LFA
TI-LFA Node Protection
R1 defines the Q Node
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
Q Node is such node which can reach destination (R3) without using protected node
10
1
Q
PLR
1
P
Protected Node

## Slide 53: FRR with TI-LFA
TI-LFA Node Protection
P Space and Q Space
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
1
Q
P
Protected Node

## Slide 54: FRR with TI-LFA
TI-LFA Node Protection
R1 builds SID-list based on each segment it found along the post convergence path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
IP
VPN
16003
24056
24045
“Ordered list of segment” for post convergence path
1
P
Protected Node
Q
16004

## Slide 55: FRR with TI-LFA
TI-LFA Node Protection
R1 programs the precomputed SID-List it in forwarding table
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
IP
VPN
16003
“Ordered list of segment” for primary path
“Ordered list of segment” for post convergence path
1
Protected Node
P
Q
IP
VPN
16003
24056
24045
16004

## Slide 56: FRR with TI-LFA
TI-LFA Node Protection
When protected node goes down R1 instantly use post convergence SID-list even before IGP converges new path
R2
R1
R3
R7
CE1
R5
R4
R6
CE2
10
n
IGP COST
1
5
1
10
1
10
1
PLR
“Ordered list of segment” for post convergence path
1
Protected Node
P
Q
IP
VPN
16003
24056
24045
16004

## Slide 57: FRR with TI-LFA
Fast Reroute with TI-LFA
SR must be implemented to have TI-LFA
100% topology coverage
Avoids micro-loop
ECMP friendly
Protects IP and LDP traffic also

## Slide 58: Lab - Demo of TI-LFA FRR vs RSVP FRR

## Slide 59: SR-TE
Segment Routing Traffic Engineering
To steer traffic through longer path
SR Policy to be implemented at ingress PE
  No more tunnel from head-end to tail-end
No state to be maintained at intermediate nodes
  No RSVP-TE means no additional signalling
Supports built-in FRR with TI-LFA
ECMP friendly

## Slide 60: SR-TE
SR Policy to be implemented at ingress PE
  No more tunnel from head-end to tail-end
No RSVP-TE means no additional signalling
  No state to be maintained at intermediate nodes
  No full mesh tunnel required
Supports built-in FRR with TI-LFA
ECMP friendly

## Slide 61: SR-TE
SR Policy
  Intended design
  Highly scalable
  Better optimization
  Automated traffic steering
Can be applied in either centralized or distributed manner
  Explicit Path: CLI or SDN Controller
  Dynamic Path: Based on constrain (i.e link delay)

## Slide 62: SR-TE
RSVP TE
R2
R1
R3
R4
CE1
R5
CE2
CE1
CE1
PATH
PATH
PATH
PATH
PATH
PATH
PATH
PATH
RESV
RESV
RESV
RESV
RESV
RESV
R1 and R2 require to maintain two separate states for two tunnels
RSVP-TE Tunnel 1
R1 > R2 > R4 > R3
RSVP-TE Tunnel 2
R1 > R2 > R5 > R3

## Slide 63: SR-TE
SR TE
R2
R1
R3
R4
CE1
R5
CE2
CE1
CE1
No tunnel required
SR Policy 1
R1 > R2 > R4 > R3
SR Policy 2
R1 > R2 > R5 > R3

## Slide 64: SR-TE
SR TE
R2
R1
R3
R4
CE1
R5
CE2
CE1
CE1
SID-List will be imposed at
source node based on SR Policy
SR Policy 1
R1 > R2 > R4 > R3
SR Policy 2
R1 > R2 > R5 > R3
IP
VPN
16003
16005
16002
IP
VPN
16003
16004
16002
Intermediary nodes don’t need to do anything extra

## Slide 65: SR-TE
SR Policy
  headend, color, endpoint
R2
R1
R3
R4
Color is used to express the intent
Color must be unique between a pair of headend and endpoint
Color is originally a numeric value
R5
CE1
CE2
CE1
CE1
R1, Pink, R3
R1, Green, R3

## Slide 66: Lab - Demo of SR TE vs RSVP TE

## Slide 67: Future Motivation
SR Control Plane Deep Dive
FRR with TI-LFA Deep Dive
SR Traffic Engineering Deep Dive
  SR Policy
  Path Validation
  Path Selection
  Traffic Steering
  On Demand Next-hop
  Flex Algo
LDP to SR Migration
SR with IPv6 Data Plane (SRv6)

## Slide 68: Thank you !!